## Slide 1
PCR AP Yield-Alert System
Complete Process Guide
Redshift -> MongoDB -> Lots & Alerts -> Teams / PDF (+ HOME data pipeline)

## Slide 2
1. Big Picture
• The plant measures every tyre for three quality dimensions.
• Raw measurements live in the Redshift data warehouse.
• app.py: reads -> cleans/renames -> stores -> lots -> compares -> alerts -> Teams/PDF.
• data_clean_process_half_hour.py: the HOME copy of the clean/merged data (no alerts).
  – Uniformity (UFM), Balancing (BAL), Geometry (GEO).
• Two modes: WITH lot size (fixed lots) and WITHOUT lot size (one lot per machine).

## Slide 3
2. The Programs
File | Role | What it does
app.py | Alert Engine | Read, clean, store, lots, yields, alerts
data_clean_process_half_hour.py | HOME Pipeline | Same read+clean+merge into HOME DBs; no alerts
trigger_mail.py | Notifier | PDFs + Teams summary + email
config.py | Settings | DB/collection names, webhook
mail_config.py | Email auth | Graph token + shared mailbox
production_db.py | Redshift connector | Opens connection, runs SQL

## Slide 4
3. End-to-End Data Flow (app.py)
• 1. Set time window. 2. Get active GT codes.
• 3. Redshift q1 (uniformity), q2 (geometry), q3 (balancing), q4 (CIMCORP).
• 4. Keep raw in memory; log to file_tracking.file_metadata.
• 5. Clean -> all_combined_data.* -> build the two merged collections.
• 6. Alerts: UFM/TBM/Curing WITH lot size, then WITHOUT lot size.

## Slide 5
4. Reading from Redshift
Query | Stage | Source | Join
q1 | Uniformity | sc_ufs.t_pertiretu | none
q2 | Geometry | sc_ufs.t_pertiretg | none
q3 | Balancing | t_pertiretg JOIN t_pertiretu | ON barcode
q4 | CIMCORP | t_pertiretu + transportationunit + ufmtesting + visualinspection | barcode; transportationunitid (LEFT)
• Filter: ptime in [start, end) AND attribute1 IN (GT codes).
• barcode = tyre key; transportationunitid links warehouse + visual results.

## Slide 6
5. Cleaning & Renaming
• mvarval10 -> rfpp_cw_kg; grade prefixes tu_/tb_/tg_ kept.
• attribute1->gt_code, tbm_stage2->tbm, cavity->curing_press, machinenum->ubno, ptime->date_of_ufm.
• Drops invalid/missing barcodes, removes duplicates, fixes types.
• Full column dictionary in the Word document (Appendix A).

## Slide 7
6. Storing Data in MongoDB
Database | Collection | Contents
all_combined_data | all_combined_{uniformity,balancing,geometry}_data | Cleaned per stage
..._merged_cleaned_data | data_merged_combined_uniform_balan_geo | Merged WITH lot size
..._merged_cleaned_data | new_data_merged_combined_uniform_balan_geo | Merged WITHOUT lot size
file_tracking | file_metadata | Load log (raw not persisted)
• CIMCORP columns merged by barcode: ufm_testing_result, visualinspection_result (+ timestamps).

## Slide 8
7. Lot Creation (Lot IDs)
• A lot = tyres from one machine + one product. TBM by tbm; Curing by press+mould; UFM by ubno.
• lot_id = STAGE_machine_model_n (e.g. TBM_12151_GT17917_1).
• machine_model_lot_id = machine_model_STAGE_machine_model_n_barcodeCount.
• previous_* chains to the prior lot.
• WITH lot size: fixed size, active machines, partial tail dropped.
• WITHOUT lot size: ALL barcodes = one lot, every machine, no null lot ids.

## Slide 9
8. Thresholds, Specs & Alerts
• Threshold shift: (current - previous) > threshold_value_<param> (default 5; cony abs).
• Spec shift: current > spec_<param> (default 0; cony symmetric).
• Yields reversed: spec shift when current < spec_yield.
• shift_occurred = threshold OR spec.
• A lot becomes a TRIGGERING alert only when >=1 machine shifted.

## Slide 10
9. Yield Calculations
Yield family | Source | Denominator | Numerator
Class OE (oe/bal/geo) | tu/tb/tg_class | {TX,T1..T8} | {T1,T2,T3,T4}
Grade (rfv, rfh1...) | grade columns | non-empty grade | grade in A/B/C/D
warehouse_yield | ufm_testing_result | {OE1, Repl} | OE1
visual_yield | visualinspection_result | {OK, NOK} | OK
• rank_counts: count tyres per grade/class when a yield deviates (e.g. tu_class_T1: 83).

## Slide 11
10. Where Alerts Are Stored
What | Database | Collection
Lot register | lot_db | lot_<stage>_table
Lot averages | average_db | averages_<stage>_table
Alert table | alert_table_final_yield | alert_<stage>_table_with_lot_size
Deviated | alert_deviated_final_yield | alert_<stage>_with_lot_size
Triggering | alert_db_virgin_yield + alert_db_final_yield | alert_triggering_<stage>_with_lot_size
• Flags: alert_flag=False, dashboard_flag=False, alert_status_check="o".

## Slide 12
11. Teams & PDF (trigger_mail.py)
• Reads alert_db_virgin_yield.alert_triggering_* where alert_flag=False.
• Recipients from alert_mail_db.alert_users (is_alert_user=True).
• Teams: MessageCard summary + deviated-parameter notes (no PDF attached).
• PDF per alert (fpdf): details, PREV/CURRENT/DIFF, SPEC, barcodes, shift data.
• Email via Microsoft Graph sendMail; batched < 20 MB / <= 180 attachments.
• On HTTP 202, alert_flag set True so it is never re-sent.

## Slide 13
12. HOME Pipeline — data_clean_process_half_hour.py
• A second, parallel pipeline: same Redshift read + clean + merge as app.py.
• Writes to a SEPARATE set of HOME databases (the home dashboard copy).
• ONLY prepares/stores data — NO lots, NO alerts, NO Teams/PDF.
• Log file: logs/log_home_{date}.txt.
• ensure_admin_collection_exists() seeds alert_mail_db admin/users if empty.
• Raw IS persisted to *_HOME; final merged = data_merged_combined_uniform_balan_geo_home.

## Slide 14
12b. HOME vs Main — Side by Side
Aspect | app.py (main) | half_hour.py (HOME)
Queries | q1-q4 | q1-q4 (identical)
Cleaning | clean_* functions | Same functions/renames
Raw persistence | Not saved (memory) | Saved to *_HOME
Combined per-stage | all_combined_data.* | all_combined_data_home.*_home
Merged collection | data_merged_combined_uniform_balan_geo | ..._uniform_balan_geo_home
Append vs refresh | Append-only | De-dup by (barcode, gt_code)
Lots/alerts/Teams/PDF | Yes | No

## Slide 15
Key Takeaways for a New Joiner
• Everything starts from barcode + GT code + ptime in Redshift.
• app.py produces data + alerts; trigger_mail.py sends them.
• data_clean_process_half_hour.py makes the HOME copy of the clean/merged data.
• An alert fires when a lot drifts vs the previous lot (threshold) or breaks spec.
• Full details, every column, and all SQL are in PROCESS_GUIDE.docx / .md.